## Slide 1: Reduced Order Models (ROMs)
RAVEN Workshop
INL/CON-19-55780

## Slide 2: Outline
Brief introduction on ROMs
ROMs and RAVEN
  Available ROMs
  RAVEN ROM workflow
RAVEN examples
  Create ROMs
  Perform sampling of ROMs

## Slide 3: ROMs: a Quick Introduction
Consider a set of N data points
Build a surrogate model
  Reduced Order Model
Inputs: Initial and boundary conditions
Output: Simulation outcome (success/failure, max clad temperature)
≅
DataObjects
(PointSet)

## Slide 4: ROMs: a Quick Introduction
Basically we are trying to reduce the complexity of the original model
Pros:
  Much faster computation of the output variable
Cons:
  Presence of error in the ROM computed values
≅
Original data (e.g., RELAP5)
ROM (e.g., quadratic regressor)

## Slide 5: ROMs: Applications
Basic steps:
  Sample original model
  Train the ROM
  Perform desired analysis with the ROM
  instead of the original model
Range of applications:
  Uncertainty quantification / Sensitivity analysis
  Probabilistic Risk Analysis (PRA)
  Accelerator for stochastic analysis (adaptive sampling)
  Prediction models
Input x
Output y

## Slide 6: ROM Modeling Within RAVEN
All modeling steps that involve ROMs are available in RAVEN
  Create ROMs from a database
  Perform statistical analysis using ROMs

## Slide 7: ROM Modeling Within RAVEN
Create a Database (PointSet)

## Slide 8: ROM Modeling Within RAVEN
Create and train a ROM from a Database

## Slide 9: ROM Modeling Within RAVEN
Perform statistical analysis using the ROM

## Slide 10: ROM Pickle
Compression/serialization scheme
Pickled object contains all the information necessary to reconstruct the object in another python script
Pickled object can be saved as a file
RAVEN Scikit-Learn ROMs can be pickled
Applications:
  Perform statistical analysis on a ROM after they have been generated and/or on a different machine
  Use pickled ROMs on separate python script (external model for RAVEN)
  Stochastic analysis for different distributions

## Slide 11: ROMs Available in RAVEN
NDspline/NDinvDistWeight: Multi-dimensional interpolators
GaussPolynomialRom/HDMRRom: Stochastic collocation
SciKitLearn (External library)
  Linear Models
  Support Vector Machines
  Multi Class
  Naïve Bayes
  Neighbors
  Tree
  Gaussian process
  Neural Network Models
ARMA: Autoregressive moving average time series model
MSR: Perform topological decomposition
PolyExponential: polynomial sum of exponentials for time-dependent
DMD: dynamic mode decomposition for time-dependent ROM

## Slide 12: RAVEN Examples

## Slide 13: Getting on the same page
This workshop will include interactive examples
paths given starting at raven
Slides are provided as well:
~> cd ~/projects/raven
~/projects/raven> git checkout devel
~/projects/raven> git pull
raven/doc/workshop/reducedOrderModeling

## Slide 14: Example Code
RAVEN samples codes
For experiment, we’ve provided some physics in a code
projectile.py
Given:
  y0, the initial vertical position
  x0, the initial horizontal position
  , the launch angle
  v0, the launch velocity
Calculates:
  , the horizontal position throughout the arc
  , the vertical position throughout the arc
  , the range or furthest point reached
  , the time of flight

## Slide 15: Workflow
Sample model Create database
Train a ROM
Pickle ROM
Train a ROM
Sample ROM
Load ROM
Sample ROM
sample_Function.xml
sample_ROM.xml
sample_pROM.xml
rom_trainer.xml
External model employed:
projectile.py

## Slide 16: Workflow
Sample model Create database
Train a ROM
Pickle ROM
Train a ROM
Sample ROM
Load ROM
Sample ROM
sample_Function.xml
sample_ROM.xml
sample_pROM.xml
rom_trainer.xml

## Slide 17: Sample a Model and Create a Database
Distributions
Steps
Samplers
Models
Databases
DataObjects
Step
Model file
Model info
Sampler
Database
DataObjects
Input file name: sample_Function.xml
<Steps>
<MultiRun name="FirstMRun">
<Input class="DataObjects" type="PointSet" >inputPlaceHolder</Input>
<Model class="Models" type="ExternalModel”>projectile</Model>
<Sampler class="Samplers" type="Grid" >grid</Sampler>
<Output class="DataObjects" type="PointSet" >outGRID</Output>
<Output class="Databases" type="HDF5" >out_db</Output>
<Output class="OutStreams" type="Print" >out_dump</Output>
</MultiRun>
</Steps>

## Slide 18: Workflow
Sample model Create database
Train a ROM
Pickle ROM
Train a ROM
Sample ROM
Load ROM
Sample ROM
sample_Function.xml
sample_ROM.xml
sample_pROM.xml
rom_trainer.xml

## Slide 19: Train and Sample a ROM
Models
Distributions
<Models>
<ROM name="ROM4" subType="NDinvDistWeight">
<Features>v0,angle</Features>
<Target>t,x,y,r</Target>
<p>3</p>
</ROM>
</Models>
Samplers
Steps
Databases
DataObjects
Input file name: sample_ROM.xml
Multi-dimensional interpolator (CROW)

## Slide 20: Train and Sample a ROM
Samplers
Distributions
Models
Steps
Databases
DataObjects
<Samplers>
<Grid name="Grid_ROM">
<variable name=”v0">
<distribution>v0_d</distribution>
<grid type=”CDF" construction="equal" steps="10">0.1 0.9</grid>
</variable>
<variable name=”angle">
<distribution>angle_d</distribution>
<grid type=”CDF" construction="equal" steps="10”>0.1 0.9</grid>
</variable>
</Grid>
</Samplers>
Finer grid
Input file name: sample_ROM.xml

## Slide 21: Train and Sample a ROM
Distributions
<Steps>
<IOStep name="extract_data4">
<Input class="Databases" type="HDF5" >out_db</Input>
<Output class="DataObjects" type="PointSet" >outGRID_y4</Output>
</IOStep>
<RomTrainer name="rom_trainer4">
<Input class="DataObjects" type="PointSet" >outGRID_y4</Input>
<Output class="Models" type="ROM" >ROM4</Output>
</RomTrainer>
<MultiRun name="RunRom4">
<Input class="DataObjects" type="PointSet" >Data1</Input>
<Model class="Models" type="ROM" >ROM4</Model>
<Sampler class="Samplers" type="Grid" >grid</Sampler>
<Output class="DataObjects" type="PointSet" >outROM_y4</Output>
</MultiRun>
...
</Steps>
Steps
Samplers
Models
Databases
DataObjects
Input file name: sample_ROM.xml

## Slide 22: Workflow
Sample model Create database
Train a ROM
Pickle ROM
Train a ROM
Sample ROM
Load ROM
Sample ROM
sample_Function.xml
sample_ROM.xml
sample_pROM.xml
rom_trainer.xml

## Slide 23: Train and Pickle a ROM
Models
<Models>
<ROM name="ROM3" subType="SciKitLearn">
<Features>v0,angle</Features>
<Target>t,x,y,r</Target>
<SKLtype>linear_model|LinearRegression</SKLtype>
<fit_intercept>True</fit_intercept>
<normalize>False</normalize>
</ROM>
</Models>
Steps
Databases
DataObjects
Inputs / Output
ROM type and parameters
Input file name: rom_trainer.xml
Notes: Add multi target ROM

## Slide 24: Train and Pickle a ROM
Models
<Steps>
<IOStep name="extract_data3">
<Input class="Databases" type="HDF5" >out_db</Input>
<Output class="DataObjects" type="PointSet" >outGRID_y3</Output>
</IOStep>
<RomTrainer name="rom_trainer3">
<Input class="DataObjects" type="PointSet" >outGRID_y3</Input>
<Output class="Models" type="ROM" >ROM3</Output>
</RomTrainer>
<IOStep name="pkDump3">
<Input class="Models" type="ROM" >ROM3</Input>
<Output class="Files" type="" >ROM3pk</Output>
</IOStep>
</Steps>
Steps
Databases
DataObjects
Create a DataObject from the Dababase
Create and train a ROM from the DataObject
Pickle the ROM and save it as a file
Input file name: rom_trainer.xml

## Slide 25: Workflow
Sample model Create database
Train a ROM
Pickle ROM
Train a ROM
Sample ROM
Load ROM
Sample ROM
sample_Function.xml
sample_ROM.xml
sample_pROM.xml
rom_trainer.xml

## Slide 26: Load and Sample a Pickled ROM
Models
Distributions
Input file name: sample_pROM.xml
<Models>
<ROM name=”pROM3" subType="SciKitLearn">
<Features>v0,angle</Features>
<Target>t,x,y,r</Target>
<SKLtype>linear_model|LinearRegression</SKLtype>
<fit_intercept>True</fit_intercept>
<normalize>False</normalize>
</ROM>
</Models>
Inputs / Output
ROM type and parameters
Samplers
Steps
DataObjects

## Slide 27: Load and Sample a Pickled ROM
<Steps>
...
<IOStep name="pk3Load">
<Input class="Files" type="" >ROM3pk</Input>
<Output class="Models" type="ROM" >pROM3</Output>
</IOStep>
<MultiRun name="RunPROM3">
<Input class="DataObjects" type="PointSet" >Data1</Input>
<Model class="Models" type="ROM" >pROM3</Model>
<Sampler class="Samplers" type="Grid" >grid</Sampler>
<Output class="DataObjects" type="PointSet" >outPROM_y3</Output>
<Output class="Databases" type="HDF5" >out_ROM3_db</Output>
</MultiRun>
...
</Steps>
Load the pickled ROM
Input file name: sample_pROM.xml
DataObjects
Models
Distributions
Samplers
Steps

## Slide 28: Exercises
Construct a ROM: 2_train_rom.xml
  Add a RomTrainer Step
Pickle a ROM: 3_pickle_rom.xml
  Use IOStep to picke a ROM
Load a ROM: 4_load_rom.xml
  Use IOStep to load a ROM
Sample a ROM: 5_sample_rom.xml
  Use MultiRun to sample a ROM
Sample a loaded ROM: 6_sample_prom.xml
  Use MultiRun to sample a pickled ROM
Evaluate a ROM: 7_evaluate_rom.xml
  Add additional MonteCarlo Sampler to evaluate a ROM
  Change the number of samples: 20, 100, 200, 1000
SciKitLearn Rom: Linear Regression
Generalized Polynomial Chaos

## Slide 29: Generalized Polynomial Chaos
Objective: overcome limitations of Monte-Carlo sampling
  High number of samples
  Computationally expensive
Polynomial representation of an output variable
  Simpler to evaluate
  Easy to get statistical moments
  Less effort and more accurate than Monte Carlo
index set of all desired polynomial orders up to order L